## Slide 1: 3D Scene Modeling: Reconstruction, Detection, and Tracking
Prof. Yi Fang
yfang@nyu.edu
Spring, 2016

## Slide 2: Announcement
Final project presentation on May 6th
Please feel free to set up appointments about Final project .

## Slide 3: Data Acquisition for MMVC & CCRL Lab
Notes: CCRL: control/robotics research lab

## Slide 4: Today’s Content
3D Scene Reconstruction
3D Detection and Tracking
3D Scene Segmentation and Semantic Labeling

## Slide 5
3D Reconstruction
3D Segmentation & Labeling
3D Tracking

## Slide 6: 3D Scene Reconstruction
3D Scene Reconstruction is the creation of 3D point cloud from multiple RGB-D images for capturing shape and appearance of real objects
The reconstruction framework consists of the following:
  Preprocess the depth map using Bilateral filter
  Convert the depth map into 3D vertex map using camera calibration matrix and evaluate the normal for each point in the vertex map
  Down sample the depth map twice by averaging nearby pixels and evaluate corresponding vertices, normal and curvatures for each map in the pyramid
  Find corresponding points in consecutive frames by using fast projective data association method assuming small motion from one frame to the other

## Slide 7: An example of 3D reconstruction
1. Kaick, A Survey on Shape Correspondence, 2010
2. Pokrass, Sparse Modeling of Intrinsic Correspondence

## Slide 8: A Review of Iterative closest point algorithm

## Slide 9: Geometric Transformation Estimation
Point cloud data set
Geometric transformation estimation
  Point cloud data sets registration
  Iterative closest point algorithm

## Slide 10: 3D Point Cloud

## Slide 11: 2D Point cloud

## Slide 12: Registration between two sets of point clouds

## Slide 13: Iterative Closest Point
The MSE objective function :
Model
Data

## Slide 14
Transform

## Slide 15: What if we do not have prior correspondence?
Solution: Assume closest points correspond

## Slide 16: Closest Point
Given two points p1 and p2 , the Euclidean distance is:
Given a point p1 and set of points Q , the closest point is defined:

## Slide 17: Iterative process
Given the correspondence determined by closest point algorithm, we could update the transformation step by step using Kabsche Algorithm
  Where is subset of M which is the set of the closest points to D

## Slide 18
After One Iteration

## Slide 19: Re-search Closest Point

## Slide 20
Step 2
ICP Algorithm

## Slide 21
Step 1
Demo Process

## Slide 22
Step 2

## Slide 23
Step 3

## Slide 24
Step n

## Slide 25
Experimental result of a LIDAR-based SLAM
A building at NYU Tandon

## Slide 26
3D Scene Reconstruction Demo

## Slide 27: Today’s Content
3D Scene Reconstruction
3D Detection and Tracking
3D Scene Segmentation and Semantic Labeling

## Slide 28: 3D Detection and Tracking
Omid Hosseini, etc, Real-Time RGB-D based People Detection and Tracking for Mobile Robots and Head-Worn Cameras, ICRA 14

## Slide 29: Tracking Scheme
Integrate the point cloud data in a 2-D histogram
This module extracts ROIs by projecting the 3D points onto the ground plane and segmenting the resulting blobs into individual objects. For each extracted 3D ROI, generate a corresponding ROI in the image plane through back-projection
Pedestrian Detection and Tracking
Trajectory Estimation

## Slide 30: Tracking Scheme
Integrate the point cloud data in a 2-D histogram:
Perform a structure labeling to classify the 3D points into three different classes ( object, ground plane, fixed structure)

## Slide 31
Fixed structure points are directly filtered out
Points that are classified as ground plane are passed to the ground plane estimation module, which fits a plane to these points using RANSAC
Points that belong to the object class are passed to the ROI (Region of Interest) processing module

## Slide 32: ROI Extraction
This module extracts ROIs by projecting the 3D points onto the ground plane and segmenting the resulting blobs into individual objects. For each extracted 3D ROI, generate a corresponding ROI in the image plane through back projection

## Slide 33: Upper Body Detection
The upper-body detector operates on depth only and consequently is limited to the range available from depth sensors (e.g., Kinect), which is usually up to 5 meters

## Slide 34: People detection
The 2D ROIs are passed to the depth-based upper-body detector, which slides a learned upper-body template over the ROIs and computes a distance matrix consisting of the Euclidean distances between the template and each overlaid normalized depth image segment

## Slide 35: Trajectory Estimation
The bounding boxes are converted to ground plane coordinates and are associated into trajectories using Extended Kalman Filters (EKFs)

## Slide 36
3D Detection & Tracking

## Slide 37: Today’s Content
3D Scene Reconstruction
3D Detection and Tracking
3D Scene Segmentation and Semantic Labeling

## Slide 38: 3D Semantic Segmentation
Semantic Segmentation deals with recognizing a category for each pixel or a voxel in a scene
State of the art semantic segmentation methods are mostly based on Deep Learning based algorithms

## Slide 39: 3D Semantic Segmentation (FCN)

## Slide 40: 3D Semantic Segmentation Result
Source: J. Xiao, SUN Database, Princeton University

## Slide 41: Good Luck on Your Final Demo!